## Slide 1: Introduction to PCB Design (with Eagle)
By: Yeo Kheng Meng (yeokm1@gmail.com)
https://github.com/yeokm1/intro-to-pcb-design-eagle
OMG Assistants (7 Dec 2015)
OMG Public (21-22 Jan 2016)

## Slide 2: About Me
Graduated from NUS Computer Science in 2015
Engineer at med-tech startup Algo Access

## Slide 3: What is a PCB?
Printed Circuit Board
A printed circuit board (PCB) mechanically supports and electrically connects electronic components using conductive tracks, pads and other features etched from copper sheets laminated onto a non-conductive substrate.
  Wikipedia
Layman definition:
  A board that lets you attach components to make a circuit.

## Slide 4: Before the PCB
Source: https://cdn.sparkfun.com/r/700-700/assets/1/3/b/5/8/50cba0dcce395fb716000000.jpg
Source: http://bunniefoo.com/novena/pvt2_release/novena_pvt2_top_sm.jpg
Point to point wire wrapping
vs
Modern PCB of Novena laptop

## Slide 5: Motivation for makers?
Space and weight constraints
Making multiple copies of a design
  Reduce mistakes in manual wiring/soldering
Aesthetics
Durability

## Slide 6: Objective of lesson
Fundamental knowledge to
Understand PCB concepts
Design a PCB
Send for manufacturing
Properly share your design with others
Efficient SMD assembling techniques

## Slide 7: Structure of a 1-layer PCB board
Usually 1.6mm thick – applies to 2-4 layers too
Silkscreen (usually white):
  Ink text. Usually used to mark out components
Soldermask (usually green):
  Prevent solder (paste) from flowing out of designated areas forming solder bridges
    Made of lacquer polymer that is “solderphobic”
  Protects copper layer from oxidation
Copper:
  Contains the traces (wires) between components
  Also contains a ground/power plane (to be explained later)
Substrate
  Gives the PCB mechanical strength and rigidity
  Usually made of FR-4, composite of fibreglass and epoxy resin
Modified from: https://cdn.sparkfun.com/assets/3/f/c/b/c/50d0c95bce395fd321000000.png

## Slide 8: Structure of a (≥2) multi-layer PCB board
  2-layer board = 2 copper layers, 4-layer board = 4 copper layers, etc
  2-layer boards good enough for most use-cases
  Silkscreen and soldermask on top and bottom only
  Vias
    Hole in PCB that electrically connects points between copper layers
    1. Blind (only for >2 layer board)
    2. Buried (only for >2 layer board)
    3. Through-hole
Source: http://techdocs.altium.com/display/ADRR/PCB_Obj-Via((Via))_AD

## Slide 9: Electronic Design Automation (EDA) Software
Software that helps you design PCBs
Eagle
  Commonly used by makers + Adafruit + Sparkfun
  Extensive library support
  User-interface so-so
  “Lite” version supports max 2 copper layers, 100 x 80 mm board size
  Not the best for high-speed designs
  Multi-platform
  Saved as XML (ASCII) files, great for version-control
Altium Designer
  Industry standard
  De-facto option for high-speed designs and complex PCBs
  Circuit simulation
  User-interface is unrivaled IMO
  File saved as binary format, terrible for version-control
  Windows-only
  Expensive: US$10K/license
KiCad
  Recently becoming more popular
  Free & open-source with no limitations
  Libraries not as common
  Saves in ASCII files, great for version-control
  Multi-platform

## Slide 10: Component packages
2D physical dimension of a component
Determines number of solder pads/sizes
Common surface-mount packages
2-pin passives (don’t rely on external power)
  0603 (0.063 inch × 0.031 inch), 0805 (0.079 in × 0.049 in), 1206 (0.126 inch × 0.063 inch), …
  SOD-123 (Small outline diode)
  MELF (Metal electrode leadless face) cylindrical SMT component
≥ 3 pins Active Components (rely on external power)
  SOT23, SOT-223-4 (Small Outline Transistor: 2.2mm pitch, 3 pins front, 4 pins total), …
Integrated circuits (ICs), usually dual-inline or square
  SOIC-16 (Small Outline Integrated Circuit 16 pins)
  SSOP-28 (Shrink small outline package 28 pins)
  TQFP-32 (Thin Quad Flat Package 32 pins)
  QFN-48 (Quad Flat No leads 48 pins)
Others
  Ports like USB, audio,
  Board to board connectors like DF40C(2.0)-70DS-0.4V
  Pin headers
  uFL antenna connector
https://github.com/yeokm1/open-source-pcb-ruler https://github.com/hemalchevli/Open-Source-PCB-Ruler

## Slide 11: PCB Design/Manufacturing Workflow
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly

## Slide 12: 1. Establish project requirements
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Circuit that blinks an LED
Customisable blink period
Customisable blink cycle
Run on CR2032 coin cells
Can run off USB power
Power switch

## Slide 13: 2. Acquire parts and prototype
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Consult data sheets to understand part selection choices
Logic Components
  Texas Instruments TLC555 timer
  Switch (C1 selection)
  C1: 33uF/100uF capacitor
  R1: 4.7kohm resistor
  R2: 10k potentiometer
  2x 0.1uF decouple capacitors
    Required according to TLC555 data sheet
Output components
  5mm 20mA Red LED
  100ohm current limiting resistor for LED
  ON Semiconductor P2N2222A NPN Transistor
  1k ohm base resistor
Power components
  2x CR2032 battery holders
  Micro-USB female connector
  3.3V low-dropout TC1262 regulator
  Diodes for battery protection
  1uF output decouple capacitor
    Required according to TC1262 datasheet
  Switch to ON/OFF circuit
*Quantity of 1 unless otherwise stated
Reference: http://www.circuitbasics.com/555-timer-basics-astable-mode/
TLC555 cannot source high currents so we use a transistor to control the LED.

## Slide 14: 3a. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Schematic defines connections between components
Open Eagle and add external libraries
Import libraries.
  Locate the libraries folder I have provided
  Drag-and-drop the *.lbr files one by one into Eagle Control Panel Libraries folder
  Right-Click on Libraries Folder -> Use all

## Slide 15: 3b. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Create and save schematic file (part and connection layout)
Create a folder on desktop “blinker”
Create new schematic *.sch: File -> New -> Schematic
Save schematic

## Slide 16: 3c. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Add all Power components first
Micro-USB female connector
  Seeed-OPL-Connector -> MICRO-USB-SMD(ZX62-B-5PA)
  Or search 320010005 obtained via Seeedstudio OPL website
  http://www.seeedstudio.com/depot/OPLopen-parts-library-catalog-c-136_138/
3.3V LDO
  bt_regulator -> TC1262 -> SOT-223-3
1uF decoupling resistor
  rcl- > CPOL-US -> CPOL-USUD-4X5,8
2x Diodes
  Seeed-OPL-Diode -> SMD-DIODE-SCHOTTKY-20V-500MA(SOD-123)
  Or search 304020028
2x CR2032 battery holders
  cr2032-large-side -> CR2032SMT
Through-hole switch
  Sparkfun-Electromechanical -> SWITCH_SPDT -> SWITCH-SPDTPTH
VCC and GND wiring net
  Just search for them…
  There are 2 functionally identical supply1 and supply2 options for VCC and GND, just pick any one you prefer.

## Slide 17: 3d. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Maneuvering and layout
Zoom with scroll-wheel
Click-drag middle mouse button to move sheet
Rotate components
  Choose Move command
  Click component “+” sign then right-click
Define component value if needed
  Right-click component -> Value
Delete object with trash icon
Wiring
  Use “Net” command
  Link components together
  Hover mouse just overlapping the contacts
  Press “Alt” increased precision key if wire cannot overlap
  Left-click to set and also to change direction

## Slide 18: 3e. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Add and wire Logic Components
Ignore TIMER_OUTPUT
TLC555 timer (dual in-line package)
  st-microelectronics -> NE555
  Not exact component but good enough
4.7kohm axial resistor
  resistor -> R-US_ -> R-US_0207/10
  2mm diameter, 7mm length, 10mm lead length
10kohm potentiometer
  Sparkfun-Electromechanical -> TRIMPOT -> TRIMPOT-PTH-KNOB
Through-hole switch
  Sparkfun-Electromechanical -> SWITCH_SPDT -> SWITCH-SPDTPTH
33uF and 100uF aluminum electrolytic ”can” capacitors
  resistor -> CPOL-US -> CPOL-USE2-5
  2mm lead spacing, 5mm diameter, polarised
2x 0.1uF ceramic decoupling capacitors
  resistor -> C-US -> C-US025-025X050
  2.5mm x 5mm area
VCC and GND
  Just search for them…

## Slide 19: 3f. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Expected result of Logic circuitry
Ignore “TIMER_OUTPUT” for now

## Slide 20: 3g. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Add and wire Output Components
Ignore “TIMER_OUTPUT” for now
100ohm and 1kohm axial resistor
  resistor -> R-US_ -> R-US_0207/10
  2mm diameter, 7mm length, 10mm lead length
5mm Red LED
  led -> LED -> LED5MM
  ON Semiconductor P2N2222A NPN Transistor (TO92 package)
  transistor -> 2N3565
  Not exact component but good enough
VCC and GND
  Just search for them…

## Slide 21: 3h. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Wiring nets
Connects between two “regions”
VCC and GND are Eagle’s provided wiring nets
We now connect logic circuit to the output circuit via TIMER_OUTPUT
Steps
  Extend a short dummy wire on one side
  Right click, choose “Label”
  Position “N$” label just beside wire
  Rename to something easier like “TIMER_OUTPUT”
  Repeat for the other end
Our custom net

## Slide 22: 3i. Design your PCB Schematic
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
12. PCB Assembly
(Grounded) Mounting holes
Allows your PCB to be secured to external case
  Grounded by screws.
  Can also use normal ungrounded mounting holes
Appears in schematic as it is an electrical connection
Mounting hole
  Grounded:
    holes -> MOUNT-PAD-ROUND -> MOUNT-PAD-ROUND3.2
  Ungrounded:
    holes -> MOUNT-HOLE -> MOUNT-HOLE3.2
  3.2mm hole fits M3 screws with slight allowance
11. Write out bill of materials (BOM)

## Slide 23: 4. Run electrical check (ERC)
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Tests if your wiring has been done properly
Not foolproof but usually good enough to detect weird or missing connections
Run ERC regularly, assign to shortcut key. Options -> Assign
Correct ALL errors
Inspect all warnings
  Correct if needed
  Ignore if you are sure
  I discourage approving

## Slide 24: 5a. Design board: place parts & wiring
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Create and save board file (board layout)
File -> Switch to board
Initial board configuration
  Adjust grid settings to mm as shown.
    View -> Grid
  Create keyboard shortcuts for commonly used functions.
    Options -> Assign
    Not case-sensitive
    End with “;”
  Enable Vector font
    Options -> User Interface
    Tick Always vector font
    Tick Persistent
CAM Processor can only convert vector fonts into Gerbers properly.
See: http://www.cadsoftusa.com/training-service/faq/#c95

## Slide 25: 6a. Setup/run design rule check (DRC)
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Design rules provided by fabricator to check if your PCB adheres to requirements
Download PCB fabricator DRU, in this case Elecrow
http://www.elecrow.com/10pcs-2-layer-pcb-p-1175.html
http://www.elecrow.com/download/Elecrow_PCB_eagle_rule.zip
*I use Elecrow as a learning example here but it does not mean I endorse this company in any way.

## Slide 26: 6b. Setup/run design rule check (DRC)
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Load DRU file just once
Press “check” to check your board or use keyboard shortcut
Rectify all errors

## Slide 27: 5b. Design board: place parts & wiring
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
General board steps
  Adjust board size to your requirements eg: 99mm x 49mm (check fabricator price point)
  Place ground/power plane on Top layer using polygon function. 1mm away from edges to ease future resizing. Set polygon name.

## Slide 28: 5c. Design board: place parts & wiring
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
General board steps
  Component placement order
    Place mounting holes
    User-facing components, like USB connectors, switches and LEDs
    Large components
    Everything else
  Wiring order (Trace width usually the size of the solder pads)
    Wire high-speed connections, avoid using vias
    Wire power connections with wider traces
    Wire everything else
  Execute DRC check and rectify if needed
  Silkscreen placement order (don’t overlap with any holes/vias/parts)
    Smash component & adjust part designators if required to minimise confusion
    Add descriptive text to certain areas to silkscreen
    Add PCB description/revision
  Miter corners
  Make sure Ratsnest gives “Nothing to do”
Tips
  Execute Ratsnest to recalculate remaining airwires’ position as much as possible after every operation
  Run DRC after you make every change to catch problems earlier
  Wire at 45 degree angles to reduce signal reflection

## Slide 29: 7. Do 3D rendering
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Use this website http://3dbrdviewer.cytec.bg/
Check for any visible errors, especially silkscreen overlap
Check for components’ “closeness”.
Go back to Step 5 if not satisfied

## Slide 30: 8. Use CAM file to generate Gerbers
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Gerber files
  2D vector format used by PCB fabricator to make PCBs for you
CAM file provided by fabricator to help you generate Gerber layer files
Download PCB fabricator’s CAM processor, in this case Elecrow
http://www.elecrow.com/10pcs-2-layer-pcb-p-1175.html
http://www.elecrow.com/download/Elecrow_Gerber_Generater_DrillAlign.zip
Use the correct CAM file according to number of layers like 2 layers
Open CAM Processor: File -> CAM Processor
Once in CAM Processor, load the CAM job as shown below
Once you are done, click “Process Job”

## Slide 31: 9. Zip up relevant Gerber files
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
See what files are required by the PCB fabricator
Elecrow’s requirements:
Go to saved folder and zip up the required files
Rightfully you should inspect your Gerber files for potential mistakes using software/websites like:
  GR-Prevue: http://www.graphicode.com/GC-Prevue_Gerber_Viewer
  http://circuitpeople.com/
  http://mayhewlabs.com/webGerber/
  But so far I don’t have any problems so I usually skip the Gerber file check step

## Slide 32: 10a. Set PCB fabrication settings
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Go to order page http://www.elecrow.com/10pcs-2-layer-pcb-p-1175.html
Basic options like PCB size, color and lead time self explanatory

## Slide 33: 10b. Set PCB fabrication settings
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Layer
  1-layer with mask both side: 1 copper layer only but you want both sides soldermask/silkscreen
  1-layer with mask one side: 1 copper layer only and you want one side soldermask/silkscreen
  2-layer: normal two copper layer boards
Copper weight:
  Copper layer thickness and amount, 1oz is usually enough
PCB Thickness:
  Typical is 1.6mm
  Elecrow can go as thin as 0.6mm for normal FR4 PCBs. Flex PCBs can go even thinner like 0.1mm
Surface finish
  HASL vs ENIG next slide
PCB Stencil
  Help you solder SMT components if you have solder paste and reflow oven/hotplate
  Frame or no frame provided. I normally go with the frame as it just costs slightly more.
Panelizing
  Squeeze many small PCBs into one piece to save space but you have to cut after receiving.
  I normally pick “Single PCB with milling” as I have no need to panelize my PCB

## Slide 34: 10c. Set PCB fabrication settings
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Others:
  Electrolytic Gold-plating, Immersion Silver, Immersion Tin, Organic Surface Protectant
HASL vs ENIG
 | HASL (lead-free) | ENIG
Acronym for | Hot Air Solder Levelling | Electroless nickel immersion gold
How it is made? | Copper surfaces covered with solder by dipping PCB in solder then blowing away | Copper surfaces covered with nickel with gold coating via immersion
Coating evenness | Uneven, don’t use for fine-pitch SMD components | Very even coat, must use if you have fine SMD components.
Durability | Reasonable, but don’t expose too long to air | Better than HASL, can last for months
Solderability (should not factor in your decision) | Great | So-so
Cost | Low | High

## Slide 35: 11. Write out bill of materials (BOM)
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Export BOM and modify.
So others can replicate your PCB
Go to Schematic view, File -> Export -> BOM
Select Parts type and CSV format as shown
Use Libreoffice to open CSV file and save in its native ODS format
  CSV not enough features, does not store column width
  Some Excel versions have difficulty opening CSV file generated by Eagle
  Open-source format
Modifying the generated BOM
  Remove mounting holes
  Collapse duplicate devices and combine their part designators
  Remove: Description, OC_FARNELL, OC_NEWARK, PROD_ID, last VALUE column
  Add: Quantity, Unit Cost , Total Unit cost (=Quantity * Unit Cost), Source webpage
  Modify the generic Eagle BOM with the actual BOM data (also add PCB Fab cost)
  Can have final Total Cost at bottom if you wish

## Slide 36: 12a. PCB Assembly
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Manual Soldering
  Soldering station
  Through-hole and SMT components
Specialised SMD Soldering techniques (with stencil and paste)
Hot air blower
Hot plate
Reflow oven

## Slide 37: 12b. PCB Assembly
1. Establish project requirements
2. Acquire parts and prototype
3. Design your PCB schematic
4. Run electrical rule check (ERC).
5. Design board: place parts & wiring
6. Setup/run design rule check (DRC)
7. Do 3D rendering
8. Use CAM file to generate Gerbers
9. Zip up relevant Gerber files
10. Set PCB fabrication settings
11. Write out bill of materials (BOM)
12. PCB Assembly
Reflow Soldering only for surface-mount components
Requires stencil and solder paste
FIRST stencil/reflow the SMD components THEN solder the through-hole components by hand.
A typical thermal profile, consult data sheet to determine optimum profile
Thermal profile based on:
  Lead vs lead-free solder paste
  Lead vs lead-free components
  Lead vs lead-free use depends on RoHS compliance
Profile Steps
  Preheat: Flux activation
  Soak: Ensure all board and components are at the same temperature
  Reflow: “Melts” solder paste and let it settle properly on the solder pads
  Cooling: Brings temperature back down at controlled rate to prevent thermal stress
Source: http://www.compuphase.com/electronics/reflowsolderprofiles.htm

## Slide 38: DIY PCB Fabrication (Toner transfer)
Materials
  Liquid Mixture: Vineger, Table Salt, Hydrogen Peroxide (H202)
  Transfer paper
  FR-4 board
Steps
  Print circuit diagram on transfer paper using laser printer
  Iron/Heat press transfer paper into FR-4 board
    https://www.youtube.com/watch?v=dvLRrXjktbE
  Mix liquid mixture of vinegar, H202 and salt
  Submerge FR-4 board in liquid mixture and agitate
  Continue until all exposed copper has been “eaten away”. (Toner covers areas you want to leave behind)
  Use a solvent/paint thinner to wipe off the toner
  Drill holes to create vias
Source, Leon Lim: http://gylim78.blogspot.sg/2014/07/the-diy-pcb-making-guide.html http://gylim78.blogspot.sg/2015/05/pcb-board-gallery.html

## Slide 39: Time to design your own board!

## Slide 40: Final Words
This is just the beginning
Practice makes perfect, the more PCBs you design/fabricate, the better you will get
Unlikely to get right on the first fabrication attempt
  2-3 times or more per design